## Telemetry from Yuneec H520

Download latest ArduPilot Mission Planner:
http://ardupilot.org/planner/docs/common-install-mission-planner.html

Load .tlog file to Mission Planner:

http://ardupilot.org/copter/docs/common-mission-planner-telemetry-logs.html

HowTo in Youtube:

https://www.youtube.com/watch?v=4IRRN5YMHJA

https://www.youtube.com/watch?v=ThVUXxOGHAE

## =====================================================
## How to download FlightLogs

ST10	ST16/ST16S
Power on RC-Controller, wait until booted up	Power on RC-Controller, wait until booted up
Connect to PC via micro USB connector (usually used for charging).	Connect to PC via micro USB connector (usually used for charging).
Doubleclick on connected device “ST10+” to open it.	Doubleclick on connected device ST16 to open it.
Doubleclick on “SD Card”.	Doubleclick on “Internal Storage” and select folder “FlightLog”.
Select folder “FlightLog” and copy (Crtl+C) or move (Crtl+X) it to your PC into a folder (Crtl+V) where you collect your FlightLogs.	Select folder “FlightLog” or “Flight2Log” and copy (Crtl+C) or move (Crtl+X) it to your PC into a folder (Crtl+V) where you collect your Flight Logs.
Select the directory “FlightLog” to open it with Q500log2kml.	Select the directory “FlightLog” or “Flight2Log” to open it with Q500log2kml.
Rename the latest FlightLog directory to avoid overwriting files with next FlightLog. Use “Archive” button in Q500log2kml to do this.	Rename the latest FlightLog directory to avoid overwriting files with next FlightLog. Use “Archive” button in Q500log2kml to do this.

## Download and open FlightLogs – example: from ST10+

Windows64bit: http://h-elsner.mooo.com/downloads/q500log2kml_en.zip
LINUX 64bit: http://h-elsner.mooo.com/downloads/q500log2kml_en.tar.gz